## Slide 1
Green Chemical Storage: Hydrogen and Ammonia
39-610 Energy Supply and Conversion
Group 11
Gabriel Goins: EST&P
James Hayes: CEE
Notes: Gabriel

## Slide 2
Introduction to Hydrogen
Hydrogen is the lightest element and is the most abundant element on Earth
It can be found by itself in a diatomic form (H2), or as part of compounds with other elements (like H2O)
Hydrogen gas properties
  Flammable
  Boiling Point is 20K
  33.6 kWh/kg H2 released from oxidation
    2H2+O2→2H2O+Energy
    Most energy dense chemical fuel by weight
    Very low energy density by volume
Notes: James

## Slide 3
History of Hydrogen
First identified in early 1500’s by Philippus von Hohenheim
  Noticed that a gas was released when metals were dissolved in sulfuric acid
Hydrogen gas used in balloons due to its low density
  Ex: Infamous Hindenburg which crashed in 1937
1789: Electrolysis of water to produce hydrogen gas was performed for the first time
1801: The idea of a fuel cell, which converts hydrogen back to electricity and water, is first introduced
1910: Haber-Bosch process to convert hydrogen to ammonia developed
First practical air-hydrogen fuel cell developed in 1959
Timeline of hydrogen technologies. (2023). In Wikipedia. https://en.wikipedia.org/w/index.php?title=Timeline_of_hydrogen_technologies&oldid=1177288012
Notes: James

## Slide 4
Applications of Hydrogen
Steel fabrication
Production of Ammonia (NH3)
  Haber-Bosch process
Petroleum refining
  Removing sulfur
High temperature heat
Energy carrier / energy storage
Electricity generation
  Gas turbines
  Fuel cells
Notes: James

## Slide 5
The “Rainbow” of Hydrogen
Color | Feedstock | Process | Relative CO2 Emissions
Black Hydrogen | Bituminous Coal | Gasification | High
Brown Hydrogen | Lignite Coal | Gasification | High
Grey Hydrogen | Methane | Steam Methane Reforming (SMR) | Medium
Blue Hydrogen | Methane | SMR with Carbon Capture and Storage (CCS) | Low-Medium
Turquoise Hydrogen | Methane | Pyrolysis | Low
Green Hydrogen | Water, Electricity from Renewables | Electrolysis | Low
Pink Hydrogen | Water, Electricity from Nuclear | Electrolysis | Low
White Hydrogen | Natural Geologic Hydrogen Sources | N/A | -
Notes: James

## Slide 6
Fossil Hydrogen Production Methods
Hydrogen Production from Coal. (n.d.). www.HydrogenAssociation.org. Retrieved October 3, 2023, from https://www.mwcog.org/file.aspx?&A=6lJMMDOHmOUL2TT9fb7pcrAAeY5PdpMxMeZbS9eJzyo%3D
Steam methane reforming. (n.d.). Retrieved October 3, 2023, from https://studentenergy.org/production/steam-methane-reforming/
Coal Gasification
Coal is exposed to water and oxygen while being heated
3C+O2+H2O→H2+3CO
  CO can react again with water to produce CO2 and more H2 (water-gas shift reaction)
Pressure Swing Adsorption used to separate H2
8 kg Coal / kg H2 produced
Emissions: 15 kg CO2 / kg H2 produced
Steam Methane Reforming
Methane and steam used as feedstock
CH4+H2O→3H2+CO
  Water-gas shift reaction can occur too
3.4 kg CH4 / kg H2 produced
Emissions: 9 kg CO2 / kg H2 produced
Notes: James
James
https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=&ved=2ahUKEwi18au82OSBAxVyk4kEHR9RB5EQFnoECCoQAQ&url=https%3A%2F%2Fgreet.es.anl.gov%2Ffiles%2Fsmr_h2_2019&usg=AOvVaw1r8M6wF0ap_93P8Vy0bv9T&opi=89978449
https://www.hydrogennewsletter.com/gh2-facts/

## Slide 7
Electrolysis of Water
Electrolytic cell used to split water into H2 and O2 gas
  2H2O(l) → 2H2(g) + O2(g)
Minimum 1.23 V must be supplied from electricity in order to accomplish this
Two main types of water electrolytic cells:
  Alkaline, which has high pH:
    Cathode (reduction): 2H2O(l) +2e-→ H2(g)+2OH-(aq)
    Anode (oxidation): 2OH-(aq)→0.5 O2(g)+H2O(l)+2e-
  Proton Exchange Membrane (PEM), which has low pH
    Cathode (reduction): 2H+(aq)+2e- → 2H2(g)
    Anode (oxidation): 2 H2O(l) → O2(g)+4H+(aq)+4e-
Cathode and anode can be made from Platinum, or Nickel in alkaline cells
Hydrogen production: Electrolysis. (n.d.). Energy.Gov. Retrieved October 3, 2023, from https://www.energy.gov/eere/fuelcells/hydrogen-production-electrolysis
Notes: James

## Slide 8
Hydrogen Production
Total global production = 95 million metric tons H2
  Equivalent to 3,200 TWh
Majority of production uses fossil fuels
Only ~0.7% (700,000 tons) of hydrogen production could be considered low emission
Global Hydrogen Review 2023. (2023). International Energy Agency (IEA). https://iea.blob.core.windows.net/assets/8d434960-a85c-4c02-ad96-77794aaa175d/GlobalHydrogenReview2023.pdf
Energy Source/Production Method | Percent of Production
SMR (Grey Hydrogen) | 62
Coal (Black/Brown Hydrogen) | 21
As an Industrial By-Product | 16
SMR with CCUS (Blue Hydrogen) | 0.6
Oil | 0.5
Electrolysis (Green/Pink Hydrogen) | 0.1
Notes: James

## Slide 9
Potential Hydrogen Resources
White hydrogen resource mostly unquantified, as black and grey have been more popular
  Recently, a 46 million ton formation was found in France
“Business as usual case” to quantify remaining grey and black/brown hydrogen
 | % of coal/NG consumption used to make hydrogen (2022) | Effective reserve of hydrogen kg (Coal or NG eq) | Effective reserve of hydrogen (Billion metric tons) | Effective reserve of hydrogen (TWh) | Reserve Lifetime (Years)
Coal | 1.9% | 2.02*10^13kg Coal | 2.525 | 83,325 | 126
Natural Gas | 7.5% | 1.106*10^13 kg NG | 3.25 | 107,347 | 51.8
Notes: Values for coal and natural gas reserve and consumption taken from BP

## Slide 10
Electrolyzer capacity limits H2 production
The future for hydrogen is very promising if we can scale up electrolyzing capacity to Net Zero Production recommendations of 560GW
  Representing 9-15 exajoules of green energy production which is on par with the International Renewable Energy Agency’s predictions of 19 exajoules of renewable energy consumption by 2050

## Slide 11
Hydrogen Conversion and Consumption
The current main consumption sectors are refining, fertilizer, and treatment/production of metals
Hydrogen as a heat source
  Burns at ~2,300 K in air
  Inefficient use of low temperature heat in homes compared to heat pumps
Hydrogen for electricity production
  Gas turbines (Brayton Cycle)
    Many newer turbines can run on a mixture of H2/CH4, or only H2
  Fuel Cells
    Used in spacecraft, vehicles, electronics
    Fuel cell vehicles
      In the US, available in California and Hawaii
      Only 56 hydrogen charging stations currently exist in US
    Currently about 350 MW of fuel cell power plant capacity in the US
      However, these facilities use mostly methane instead of hydrogen
    Types of fuel cells
      Alkaline (~375 K)
      High Temperature (Solid oxide, molten carbonate) (>900 K)
Notes: James

## Slide 12
Hydrogen and Ammonia as Energy Carriers
Green hydrogen as a means to store excess renewable electricity
  Variable renewables like Solar PV and Wind
    Difficult to scale generation to meet demand at any given time
    Issue of the “Duck Curve”
  During times of low demand, store electrical energy by converting to hydrogen
  Convert back to electricity will a fuel cell or turbine during times of high demands
Confronting the duck curve: How to address over-generation of solar energy. (n.d.). Energy.Gov. Retrieved October 9, 2023, from https://www.energy.gov/eere/articles/confronting-duck-curve-how-address-over-generation-solar-energy
Source: US Department of Energy
Notes: James
https://www.energy.gov/eere/articles/confronting-duck-curve-how-address-over-generation-solar-energy

## Slide 13
Hydrogen and Ammonia as Energy Storage/Carriers
Storing Hydrogen
  As a gas: Pressurized Tanks, Geologic reservoirs like salt caverns, Pipelines
  As a liquid: Cryogenic Tanks (Temperatures < 20 K)
    Extremely energy intensive, not done often
Ammonia as an alternative method of storing hydrogen
  Use Haber-Bosch process to convert hydrogen and nitrogen gas to ammonia
    Mature technology/process
    Cracking process to convert ammonia back to hydrogen
  Liquified ammonia (Temperatures < 240 K)
    Less energy loss during transport/storage than liquid hydrogen
  Potential Issues:
    Significant temperatures and energy needed for Haber-Bosch process
    Another ~20 MWh/ton H2 must be input, compared to 33.6 MWh/ton H2 which can eventually be recovered by oxidizing hydrogen
Ammonia’s role in a net-zero hydrogen economy. (n.d.). Kleinman Center for Energy Policy. Retrieved October 3, 2023, from https://kleinmanenergy.upenn.edu/research/publications/ammonias-role-in-a-net-zero-hydrogen-economy/
Notes: James

## Slide 14
Hydrogen Consumption
Global consumption is 95 million metric tons
  Of which about 45 MT is for oil refining, rest for other industry (e.g. fertilizer and steel)
Currently, virtually no hydrogen is used for vehicles or for power storage+generation
To meet Net Zero Emissions by 2050, an expansion in these alternative uses is needed
  55 MT/yr expansion in capacity by 2030 for use in these sectors
Source: IEA.
Notes: James

## Slide 15
Breakdown of Hydrogen around the World
Current US production is about 10 million tons/yr hydrogen
  95% is made with SMR (grey/blue)
  1% from electrolysis (green/pink)
In the US, Inflation Reduction Act of 2022 offers subsidies depending on emissions of hydrogen, with 4 different tiers
NEOM Green Hydrogen Facility in Saudi Arabia set to start up in 2026
  220,000 tons/yr H2
  1.2 million tons/yr NH3
  4 GW solar PV and wind farm
Source: IEA.
Source: IEA.
Notes: James

## Slide 16
Hydrogen in China
China is the world’s largest producer and consumer of hydrogen
Total Production and Consumption in 2021 = 36,480,000 metric tons
Over 99.9% of hydrogen in China is used for industrial purposes (e.g. fertilizer, refining, etc.)
Green hydrogen only makes up 0.05% of production as of 2021
China has set a target for 2025
  100,000-200,000 tons/yr green hydrogen production
  Associated reduction of 1-2 million tons CO2 emissions
Bocca, R., Liu, W., & Zhu, S. (2023). Green Hydrogen in China: A Roadmap for Progress. World Economic Forum (WEF). https://www3.weforum.org/docs/WEF_Green_Hydrogen_in_China_A_Roadmap_for_Progress_2023.pdf
Hydrogen Type | Production (tons/yr)
Black/Brown | 19,590,000
Grey | 7,730,000
Green | 17,000
As an Industrial By-Product | 6,400,000
Total | 36,480,000
Recent green hydrogen facilities have been located in Inner Mongolia and Xinjiang regions of China
Notes: James

## Slide 17
Green Hydrogen Facilities in China
Concerns have been raised about Kuqa facility and its ability to meet capacity using only the Solar PV in the facility.
According to BloombergNEF, its 361 MW solar farm could only meet 58% of the energy needs at maximum capacity.
  Therefore, Sinopec may need to buy energy from the grid
  If they cannot source renewable/low emission energy, then they may have to rely on fossil, such that hydrogen will not be green
Collins (l_collins), L., & Yihe (x_yihe), X. (2023, May 26). World’s largest green hydrogen project—China’s 260MW Kuqa facility—To be commissioned at the end of May. Hydrogen News and Intelligence | Hydrogen Insight. https://www.hydrogeninsight.com/production/world-s-largest-green-hydrogen-project-chinas-260mw-kuqa-facility-to-be-commissioned-at-the-end-of-may/2-1-1457242
Facility | Production Capacity (tons/yr) | Electricity Source | Storage Capacity (m3) | Transmission Capacity (m3/hr) | Capital Expense ($M)
Kuqa (2023) | 20,000 | Solar PV | 210,000 | 28,000 | 414
Narisong (2023) | 10,000 | Solar PV | - | - | -
Ordos (Upcoming) | 30,000 | Wind and Solar PV | 288,000 | - | -
Notes: James

## Slide 18
LCOE for Hydrogen
International Energy Agency
Levelized cost of energy+. (n.d.). Https://Www.Lazard.Com. Retrieved October 3, 2023, from https://www.lazard.com/research-insights/levelized-cost-of-energyplus/
Notes: James

## Slide 19: Benefits/Disadvantages
Notes: Gabe

## Slide 20
China is on track for scaling up targets
It is estimated that hydrogen will account for 10–12% of China’s energy consumption by 2050 and green hydrogen is expected to reach price parity with currently cheaper gray hydrogen within a few years.
The reasons:
Provincial Policy
Research and development support for hydrogen led to increased patent applications
  Chinese patents for hydrogen exceeds that of the rest of the world combined
  R&D expenditure in China for hydrogen surpassed the EU and US combined
Academia
  40% of academic papers published on green hydrogen were from China
Notes: Before going into what policy I would recommend have to touch on what is already working in China

## Slide 21
Provincial Policy
Provincial policy targets are more ambitious than the ones of the national strategy.
  120 green hydrogen production projects at different stages of development in China
  Policy focused on general industry development in the short term greening is second priority.

## Slide 22
Research and development
Current forecasts estimate China will reach 38 GW of electrolyzer capacity by 2030 and they currently account for 35 percent of global electrolyzer manufacturing capacity
  Three Chinese companies dominate the Chinese market for alkaline electrolyzers: PERIC Hydrogen Technologies, Cockerill Jingli Hydrogen, and Tianjin Mainland Hydrogen Equipment.
China’s nascent green hydrogen sector: How policy, research and business are forging a new industry | Merics. (2022, June 28). https://merics.org/en/report/chinas-nascent-green-hydrogen-sector-how-policy-research-and-business-are-forging-new

## Slide 23
Recommendations: What to improve?
Unlike other countries where decarbonization is the core of ramping up green hydrogen, China is taking a more capitalistic approach which explains the conservative national policy.
Our recommendations:
Specifically for China, rapid expansion in hydrogen production and diversification of hydrogen supply away from coal gasification is imperative to meet future industrial demand
Quality over quantity: R&D should be focused on improving technologies and increasing capacity
  Focus on green over blue (which is less established in China)
Invest in hydrogen education to increase hydrogen production workforce
National policies and subsidies to incentivize green hydrogen production and raise implement carbon taxes
  Like the IRA in the US
Incentivize startup green hydrogen companies as monopolies will ruin the goal
Notes: IRA Provides a tax credit for investment in renewable energy projects.

## Slide 24
Bibliography
Timeline of hydrogen technologies. (2023). In Wikipedia. https://en.wikipedia.org/w/index.php?title=Timeline_of_hydrogen_technologies&oldid=1177288012
Hydrogen Production from Coal. (n.d.). www.HydrogenAssociation.org. Retrieved October 3, 2023, from https://www.mwcog.org/file.aspx?&A=6lJMMDOHmOUL2TT9fb7pcrAAeY5PdpMxMeZbS9eJzyo%3D
Steam methane reforming. (n.d.). Retrieved October 3, 2023, from https://studentenergy.org/production/steam-methane-reforming/
Hydrogen production: Electrolysis. (n.d.). Energy.Gov. Retrieved October 3, 2023, from https://www.energy.gov/eere/fuelcells/hydrogen-production-electrolysis
Global Hydrogen Review 2023. (2023). International Energy Agency (IEA). https://iea.blob.core.windows.net/assets/8d434960-a85c-4c02-ad96-77794aaa175d/GlobalHydrogenReview2023.pdf
Confronting the duck curve: How to address over-generation of solar energy. (n.d.). Energy.Gov. Retrieved October 9, 2023, from https://www.energy.gov/eere/articles/confronting-duck-curve-how-address-over-generation-solar-energy
Ammonia’s role in a net-zero hydrogen economy. (n.d.). Kleinman Center for Energy Policy. Retrieved October 3, 2023, from https://kleinmanenergy.upenn.edu/research/publications/ammonias-role-in-a-net-zero-hydrogen-economy/
Bocca, R., Liu, W., & Zhu, S. (2023). Green Hydrogen in China: A Roadmap for Progress. World Economic Forum (WEF). https://www3.weforum.org/docs/WEF_Green_Hydrogen_in_China_A_Roadmap_for_Progress_2023.pdf
Collins (l_collins), L., & Yihe (x_yihe), X. (2023, May 26). World’s largest green hydrogen project—China’s 260MW Kuqa facility—To be commissioned at the end of May. Hydrogen News and Intelligence | Hydrogen Insight. https://www.hydrogeninsight.com/production/world-s-largest-green-hydrogen-project-chinas-260mw-kuqa-facility-to-be-commissioned-at-the-end-of-may/2-1-1457242
Levelized cost of energy+. (n.d.). Https://Www.Lazard.Com. Retrieved October 3, 2023, from https://www.lazard.com/research-insights/levelized-cost-of-energyplus/
China’s nascent green hydrogen sector: How policy, research and business are forging a new industry | Merics. (2022, June 28). https://merics.org/en/report/chinas-nascent-green-hydrogen-sector-how-policy-research-and-business-are-forging-new
Notes: https://merics.org/en/report/chinas-nascent-green-hydrogen-sector-how-policy-research-and-business-are-forging-new
https://arc-group.com/china-hydrogen-energy/
https://www.csis.org/analysis/chinas-hydrogen-industrial-strategy
https://www.iea.org/energy-system/low-emission-fuels/hydrogen

## Slide 26
Innovative predictions for this resource
Steelmaking
Combining power with heat generation
Fuel cells

## Slide 27
Local benefit
Hydrogen for fuel cell vehicles will decarbonize transportation and energy sectors
Job creation
Less reliant on coal (currently at 55% of total energy mix)
Climate-resilient energy transition solves issues with energy security as diverse energy mixes supports climate change adaptation.

## Slide 28
Notes: Gabe